## Slide 1: Yap Renewable Energy Development Project
PPA Conference Palau 2018
Dean Haley – 28 July 2018

## Slide 2: About Entura
    One of the world's most experienced specialist power and water consulting firms
    Part of the Hydro Tasmania group - backed by more than 100 years of creating energy and maintaining power and water assets
    Services covering every aspect of major power and water projects, from strategy, planning, design and construction through to operation, maintenance, risk management and training
    Over 200 staff; expanding business opportunities nationally and internationally
    Broad range of clients across the Asia-Pacific region including:
      all levels of government
      electricity and water utilities
      developers
      funding agencies (World Bank, ADB)

## Slide 3: solutions across the whole lifecycle
Notes: We partner with clients to deliver practical and commercially sound solutions across the whole lifecycle of power and water assets, helping them to manage risks and achieve valuable outcomes

## Slide 4: Hybrid renewables
As the world increasingly embraces renewable electricity generation, and transitions away from costly or emissions-intensive technologies, the need is growing for hybrid renewable energy assets that combine multiple forms of generation and storage.
Our services include:
    renewable energy roadmaps, conception and master planning
    feasibility studies and concept designs
    power systems and grid connection studies
    due diligence assessments
    tender and bid responses
    planning and environmental approvals
    front-end engineering design including power systems modelling, integration design and control design and interface specification
    detailed designs, technical specification, procurement and factory testing
    control code and HMI (operator screen) design and preparation
    owner’s engineer role
    project management of site works including construction, installation, pre-commissioning, unit commissioning, system integration commissioning and initial operation
    asset management plans
    operator training
    remote system support
    web dashboards and app development for mobile devices

## Slide 5: Renewables are our future
Yap State Renewable Energy Transition in Partnership with ADB and FSM

## Slide 6: Presenter - Dean HAley
Renewable Energy Engineer with Entura
Entura were awarded the Design and Construction Supervision (DSC) contract on 29th April 2014
My role in this project was YREDP Team Leader
Implementing Agency – Yap State Public Service Corporation (YSPSC)
  Faustino Yangmog – General Manager
  Victor Nabeyan – Assistant General Manager and PMU Project Manager
  Vincent Bouet – YSPSC Chief Engineer
Funding Agency - ADB
  Energy Specialist - Mike Trainor

## Slide 7: National Energy Policy

## Slide 8: Yap State Energy Action Plan
The National Vision statement for Energy is
    To improve the life and livelihood of all FSM citizens with affordable, reliable and environmentally sound energy.
  The National Objective for Energy is
    To promote the sustainable socio-economic development of FSM through the provision and utilization of cost-effective, safe, reliable and sustainable energy services.
  Yap State’s Energy Action Plans
    To become less dependent on imported sources of energy by having an increased share of renewable energy sources
      30% of energy coming from renewable sources by 2020
      50% improvement in energy efficiency by 2020
      50% of energy coming from renewable sources by 2030

## Slide 10: The Entura Team

## Slide 11: Working Collaboratively with yspsc

## Slide 12: Yap located in the caroline islands

## Slide 13: Yap - A Traditional Island capable of modern transition

## Slide 14: A Modern fully Integrated Hybrid RE Power System

## Slide 15: Scope Of Works
Wind resource and energy estimate feasibility confirmation
Power System Studies
Confirm and Develop Power System Architecture
Procurement Planning
Preparation of both Technical and Commercial Bidding Documentation
Bidding process including bid evaluation
Owners Engineer during detailed design
Social safeguards planning and implementation monitoring
Environmental safeguards planning and implementation monitoring
Construction Supervision
Witness Commissioning and Acceptance

## Slide 16: Combining Resources to reduce variability
Combining resources to reduce variability.
Solar and wind resources are often negatively correlated: Solar power peaks in the summer, whereas wind tends to peak in the winter. On the other hand, solar power peaks during the day, while winds tend to be stronger in the afternoon and at night. These correlations make it possible to mix wind and solar resources to yield a combined power output that mimics the demand curve, a phenomenon called natural balancing
Wind and solar energy is a fast-growing share of the global energy mix. But integrating them into power-system operations requires significant adaptations to compensate for their variability. Solutions include increasing the amount of flexible generation within the system, combining, and dispersing variable resources to smooth aggregate output, expanding the transmission network, using smart technology to control supply and demand, and storing electricity.

## Slide 17: Power System Studies – Grid Stability
To estimate the future high renewable penetration power system performance, four worst-case scenarios were conducted and studied:
    Wind farm trip with a single diesel online
Wind farm trip with two diesels online
Colonia feeder trip with a single diesel online
Colonia feeder trip with two diesels online
These simulation scenarios showed that the system frequency and voltage will venture outside their normal operating limits during critical events.
Installation of high speed diesel engines will provide Yap power system with fault ride through capability during the critical events with minimal or no loss of customer load.

## Slide 18: RE Integration
Wind and solar energy is a fast-growing share of the global energy mix. But integrating them into power-system operations requires significant adaptations to compensate for their variability. Solutions include increasing the amount of flexible generation within the system, combining, and dispersing variable resources to smooth aggregate output, expanding the transmission network, using smart technology to control supply and demand, and storing electricity.

## Slide 19: Automated Integration and Control System
The control systems of today’s smart power-distribution grids have evolved significantly. Such systems improve system reliability by reducing the frequency and duration of outages. They also optimize asset utilization and increase power quality. But the scale of automation and the ultimate configuration of the system need to be considered carefully with each client. The decision to proceed must be based on a sound economic evaluation; it cannot simply echo the mantra of automation.

## Slide 20: Original Power House

## Slide 21: Removal of Redundant Diesel Generators

## Slide 22: Replace With New High Speed Diesel Generators
2 * 1650kw Cat 3615C Diesel Gensets

## Slide 23: High speed Diesels
1 * 800 kw Cat Diesel genset

## Slide 24: Replace redundant Switchgear with New MV Switchgear

## Slide 25: Upgrade to the fuel Storage and Transfer System including Installation of New Day Tanks

## Slide 26: Power House Commissioning

## Slide 27: Community consultation

## Slide 28: Wind Power
    3 * 275 kW Vergnet wind turbine generators
    Key features
      Guy wired tilt down tower for typhoon survival
      Tilt down allows for ease of construction, operation and maintenance
      Smaller crane size required than for typical monopole wind turbine towers.

## Slide 29: Wind turbine Site identification and identification of constraints

## Slide 30: Identification and Protection of Historical Sites for preservation & Environmental Safeguards

## Slide 31: Windfarm Site Clearance

## Slide 33: Windfarm Construction

## Slide 34: Solar PV
 | Existing PEC Solar to be integrated New Grid Connected Solar PV Total Solar PV | 200 kWp 308.5 kWp 508.5 kWp
1 | Sports Complex | 194.5 kWp
2 | Public Safety Building | 25 kWp
3 | Early Childhood Education Building | 50 kWp
4 | Water Treatment Plant | 13 kWp
5 | Public Works Building | 26 kWp

## Slide 35: Existing PEC Solar 200 kw

## Slide 36: Sports Complex 194.5KW

## Slide 37: Solar Installation by YSPSC

## Slide 38: Public Safety Building 25kW

## Slide 39: Water Treatment Plant 13 KW

## Slide 40: Civil Engineering and Maintenance Building 26 kW

## Slide 41: Early childhood centre 50 kW

## Slide 42: Island Wide Communications Network

## Slide 43: Opening Ceremony
Left to Right – Hon. Ted Rutun (Yap Legislature Speaker), Jim Lynch (Deputy Director General, Pacific Department, ADB), Hon. Tony Ganngiyan (Yap Governor), HE Peter Christian (FSM President), James Gilmar (Chairman, YSPSC Board of Directors).

## Slide 44: Integration And Control

## Slide 45: Current performance – 1 hr period

## Slide 46: Operation

## Slide 47: Hybrid Grid

## Slide 49: Achievements to date
Since the commissioning, no outage has been attributed to the introduction of the renewable energy facilities, Wind & Solar.
The reliability was not impacted.
The weather conditions were not favourable to produce important renewable energy. A few windy conditions, with a lot of variability of RE have shown that the supervision and control system is performing as expected, curtailing RE if necessary to keep stability and diesel generator(s) under minimum load.
The Dynamic Spinning Reserve plays its role and we can observe the small peak generator coming on line when necessary.
The system reached 60% of RE penetration without any energy storage.
Under particular conditions, the small peak generator connects & disconnects quite often, thus we look forward to the introduction of an Energy Storage System.
The full RE potential will be observed during the trade winds season. At present, the rainy season shows limited RE production in very few occasions.

## Slide 50: Diesel Displacement
Average diesel displacement:
So far, the wind farm has produced 602 MWh
    MP1 318.4 MWh
    MP2 135.1 MWh
    MP3 148.5 MWh
The solar farms (ABD project only, PEC excluded) have produced 264.167 MWh since their installation.
Approximate Diesel Displacement so far:
    866167 kWh / 14 = 61,869 US Gall. @ $USD3.9/ gallon - $USD241,3000
Diesel displacement in non-wind period ie Solar only:
    264167 kWh / 14 = 18,869 US Gall

## Slide 51: Ingredients For Success
Commitment from National and State Governments
Capable and Competent Executing Agency
    Executive management
    Operational management
    Operators
Community Engagement
Renewable readiness
Acceptance, Resilience and Preparation for Disruption

## Slide 52: Contacts
Dean Haley – Senior Project Manager
  E: dean.haleyl@entura.com.au
  P: +61 (0)407 515 447