## Slide 1
R
Small Roof-top Solar Metering
and Payment

## Slide 2
Roof-top private solar for residences
1kW to 3 kW residential solar
Off-sets house load
About the same usage every day

## Slide 3
Roof-top solar for commercial facilities and government buildings
Commercial/Government building solar (typically around 10 kW up to 50kW or more)
Commercial/Governmental loads often have a much lower load on weekends and therefore surplus solar

## Slide 4
Metering of small
grid-connected solar installations
Dual meters
Single meter providing net metering by reversing
Single meter without reverse metering
“solar” meter
Prepayment meter
“Smart” meter

## Slide 5
Dual Meters
Solar is connected directly to the grid through one meter
Grid electricity is delivered to the building through the other meter
Grid electricity minus solar electricity = the payment required from the customer to the utility or credit to be received by the customer for excess energy delivery
This is the preferred approach for metering in the islands

## Slide 6
Single meter that provides
net-metering directly
The solar is connected on the building side of the meter and surplus energy from the solar runs the meter backward. Negative reading indicates a credit, positive reading indicates a billing amount.
Does not show either the customer or the utility the amount of solar energy or grid energy used by the building, only the net energy

## Slide 7
Single meter without reversing
Solar connected on building side of the meter
Does not run backward when solar output exceeds building use
Some meters may allow the excess solar to enter the grid (providing the utility free power)
Most “one-way” meters will block energy flow from the building to the grid so utility does not receive the excess energy, it is lost to both utility and customer.
Benefits neither the utility nor the customer

## Slide 8
“Solar” meter
A meter specifically designed for grid-connected solar. Has two readings, one for solar generation and one for total energy used by the house
Expensive

## Slide 9
“Smart” meter
Utility can manage the metering of charges for grid power and credits for solar generation remotely. Most useful for utilities with high peak load generation costs and large diverse service area
Typically shows only the net flow of power unless more expensive solar metering is specified. Solar generally not directly metered
Can meter at different tariffs for different times of the day
Expensive

## Slide 10
Solar when pre-payment meters
are used
Solar is connected to the grid directly and a separate meter is used to measure solar delivery
Credits for solar are provided the customer through the provision of top-up vouchers for the kWh shown on solar meter readings
Only practical for flat tariffs (the same charge per kWh for all usage)

## Slide 11
Payment arrangements for solar inputs
Feed-in tariff for all generation
Solar offsets grid energy use for the building only (no payment or credit for surplus solar generation)
Net metering – solar directly offsets grid usage and surplus can be time shifted for later use by the customer or paid for by the utility using a ‘Feed In Tariff’

## Slide 12
Feed-in tariff – Rate Paid for Solar kWh input
Specific payment per kWh given for surplus power delivered to the grid
Solar kWh that offsets grid kWh is effectively valued at the tariff rate since the customer saves that amount (and the utility loses that amount)
Payment is strongly related to fuel offset cost but is best termed ‘avoided cost of energy delivery’
Government may make the feed-in payment higher than the grid power tariff to encourage installing more solar
May be lower than fuel offset cost or even zero if the utility does not want to encourage private solar for customers

## Slide 13
Offset of grid energy use only
Effectively zero feed-in payment for surplus energy.
OK for the customer whose main energy use is during the day
Commercial/government customers usually ok
Residential customers usually not, most use of energy is at night

## Slide 14
Net-metering
Credit to pay for future energy use is provided when surplus energy is delivered to the grid
Effectively feed-in tariff is the grid power tariff for the customer when full kWh credit is given for surplus
Usually credits are cleared periodically so they do not accumulate beyond reasonable levels

## Slide 15
Frequency of clearing surplus
solar kWh credits
Monthly
For countries with reasonably constant solar over the year
Annually
For countries with seasonal solar clearing credits at the beginning of the high solar season makes sense
A feed in tariff may be paid when resetting surplus solar credits

## Slide 16
DISCUSSION